## Slide 1
▦
COURSE NOTES · IOT SECURITY
Security and Safety
Systems · Network · Application Security
with the ARMET Approach
AUDIENCE
Computer Science / IT Students
MODULES
9 Concept Topics with Block Diagrams
DURATION
~45 min Lecture
IoT-SEC · 2026
VOL. 01
Notes: Welcome students. This lecture deck covers nine concept topics in IoT security, structured as a learning module. Each topic is presented with a definition, a block diagram, real-world examples, and applications — so you get both the conceptual model and the engineering intuition behind it. We begin with the IoT security landscape and end with privacy and dependability, with the ARMET hardening approach as the centerpiece methodology that ties everything together. By the end of this forty-five-minute session, you should be able to reason about IoT threats across perception, network, and application layers, and apply a structured hardening workflow to a microcontroller-class device.

## Slide 2
AGENDA
Nine Concepts, One Secure Stack
Each topic pairs a concept slide with a block diagram, examples, and real-world applications.
DECK · 2026
9 / 9
01
Introduction
Why IoT security matters: scale, threats, layered defense
02
Systems Security
Hardware roots of trust, secure boot, TEEs
03
Network Security
Confidentiality, integrity, and authenticity in transit
04
Generic Application Security
AuthN, AuthZ, crypto, secure update
05
Application Process Security & Safety
Functional safety, SIL, SIF, hazard analysis
06
Reliable & Secure by Design
Shift-left, threat modeling, defense in depth
07
Run-Time Monitoring
IDS, anomaly detection, live response
08
The ARMET Approach
A 7-step hardening methodology for microcontrollers
09
Privacy & Dependability
RAS triad, GDPR, fault → failure chain
CAPSTONE · ARMET
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
02 / 21
Notes: This deck is organized into nine concept topics. Each topic follows the same teaching pattern — first a concept slide that defines the term and gives examples, then a dedicated block diagram slide that visualizes the architecture or flow, and throughout, live real-world examples and applications. We start with a broad introduction to IoT security, then move down the stack from systems to networks to applications, then up again into process safety, design-time methodology, runtime monitoring, and finally the ARMET hardening approach and privacy and dependability. Treat ARMET as the capstone — it ties together many of the earlier concepts into a single seven-step hardening workflow you can apply to a microcontroller-class device today.

## Slide 3
01 · INTRODUCTION
CONCEPT · LECTURE 1 / 9
What is IoT Security?
IoT Security is the practice of protecting Internet-of-Things devices, their data, and the networks they connect to, from confidentiality, integrity, and availability attacks. Unlike traditional IT, IoT adds constrained devices, physical exposure, long lifecycles, and heterogeneous protocols — making security a multi-layer problem rather than a single firewall.
Scale — 75+ billion connected devices by 2027, each a potential attack surface.
Risk — Average IoT breach cost reaches $5.4M, with 57% of devices vulnerable to medium/high-severity attacks.
Layered defense — Security must span perception (sensors), network (transit), and application (logic) layers.
✦
75B
Connected devices by 2027
⚠
57%
IoT devices vulnerable to attacks
$
$5.4M
Avg cost of an IoT-related breach
✦
24K
Unique malware samples seen per day
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
03 / 21
Notes: We open with a working definition: IoT security is the discipline of protecting connected devices, their data, and the networks they ride on, against attacks on confidentiality, integrity, and availability — the CIA triad. The reason we dedicate a full module to IoT security is that it differs materially from enterprise IT. Devices are resource-constrained — many cannot run full TLS or antivirus agents. They are physically exposed, often deployed outdoors or in homes where attackers can touch them. They have lifecycles of ten-plus years, far longer than typical phones or servers. And they speak dozens of protocols — Zigbee, LoRa, BLE, MQTT — each with its own threat model. The four statistics on the right show the scale of the problem: 75 billion devices by 2027, more than half vulnerable, million-dollar breach costs, and tens of thousands of new malware samples daily.

## Slide 4
01 · INTRODUCTION
IoT Security — Layered Architecture
Three layers, three threat surfaces, three sets of controls.
BLOCK DIAGRAM
01 · PERCEPTION
Sensors
Actuators
RFID
Cameras
Examples: temperature sensor, smart-lock solenoid, RFID badge reader
02 · NETWORK
Wi-Fi
BLE
Zigbee
LoRa
MQTT
6LoWPAN
Examples: TLS 1.3 over Wi-Fi, DTLS for constrained BLE, IPSec tunnels to cloud
03 · APPLICATION
Cloud
Mobile App
Analytics
Firmware OTA
Examples: AWS IoT Core, Google Cloud IoT, custom mobile companion app
LIVE EXAMPLE
Mirai botnet (2016) compromised 600K+ IoT cameras at the perception layer using default Telnet credentials, then flooded Dyn DNS at the network layer — taking down Twitter, Netflix, and Reddit for hours.
Application — Smart City Surveillance
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
04 / 21
Notes: The IoT security problem decomposes naturally into three layers, each with its own threats and controls. The perception layer is the physical edge — sensors, actuators, RFID tags, and cameras. Threats here include physical tampering, side-channel attacks, and firmware extraction. The network layer carries the data — Wi-Fi, BLE, Zigbee, LoRa, and the messaging protocols that ride on top, like MQTT. Threats here are eavesdropping, replay, man-in-the-middle, and DDoS. The application layer is the cloud, mobile, and analytics tier — and over-the-air firmware, which is often the softest target. The Mirai botnet is the canonical live example: it compromised perception-layer cameras using default Telnet credentials, then used them as a launchpad for a network-layer DDoS against Dyn DNS, which cascaded into application-layer outages at Twitter, Netflix, and Reddit. One attack, three layers.

## Slide 5
02 · SYSTEMS SECURITY
CONCEPT · LECTURE 2 / 9
Hardware Roots of Trust
Systems security is the lowest layer of defense — the silicon, firmware, and operating-system primitives that establish trust before any application runs. Without a verifiable hardware root, every higher layer inherits an untrustworthy foundation.
Secure Boot — verify cryptographic signatures at every stage from ROM to kernel, halting on mismatch.
Trusted Execution Environment (TEE) — isolated enclave (e.g. ARM TrustZone) for keys, biometrics, and DRM.
Hardware Crypto Engine — on-chip AES, ECC, TRNG, and key storage in tamper-resistant secure elements.
⛨
TPM 2.0
Trusted Platform Module, discrete crypto chip
⚿
ARM TrustZone
TEE isolating secure world from normal world
▦
Secure Element
SE chip for key storage (e.g. NXP A71C)
☁
HSM
Hardware Security Module for cloud-side CA
⚡
LIVE EXAMPLE — In 2018, a hardware root-of-trust flaw in certain NVIDIA Tegra chipsets allowed the Nintendo Switch boot ROM to be bypassed, enabling arbitrary code execution at the earliest boot stage.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
05 / 21
Notes: Systems security is the foundation. If an attacker controls the silicon or the boot path, no application-layer defense can save you. The key idea is a root of trust — a small piece of immutable, cryptographically verifiable code, often burned into ROM at manufacture time, that verifies the next stage before executing it. That next stage verifies the next, and so on — a chain of trust that runs from power-on to a running OS. The four hardware primitives on the right are the building blocks: TPM 2.0 for PCs and servers, ARM TrustZone for SoCs, dedicated secure elements for keys, and HSMs on the cloud side. The Nintendo Switch boot ROM exploit from 2018 is a textbook case — a single unpatchable flaw in the Tegra X1's boot ROM gave attackers permanent control of the device, because the root of trust itself was broken.

## Slide 6
02 · SYSTEMS SECURITY
Chain of Trust — From Silicon to Application
Each layer verifies the next; a single breakable link compromises the whole chain.
BLOCK DIAGRAM
06 · APPLICATION
▦
Weather App, Smart Lock UI
Verified at install time
05 · OS KERNEL
▦
Linux / FreeRTOS / Zephyr
Signed kernel image
04 · BOOTLOADER
➤
U-Boot / Coreboot
Verified by ROM stage
03 · SECURE BOOT ROM
⚿
Immutable mask ROM
Vendor burned at factory
02 · HARDWARE ROOT
⚿
eFUSE, OTP, Public-key hash
Anchored in silicon
01 · SILICON SOC
✦
ARM Cortex-M / RISC-V
TrustZone-M / PMP
APPLICATIONS
Smart meters verify firmware signatures before accepting OTA updates.
Medical insulin pumps lock down actuator control to signed code only.
Automotive ECUs enforce Secure Boot to prevent tuning/ECU mod attacks.
Chain-of-Trust model
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
06 / 21
Notes: The chain of trust is built bottom-up. At the bottom is the silicon — the SoC itself, with hardware isolation features like ARM TrustZone-M or RISC-V PMP. On top of that, a one-time-programmable key hash — typically burned into eFUSE at manufacture — anchors the root of trust. The mask ROM is the first code that runs at power-on, and it is immutable: it cannot be patched even by the vendor. The ROM verifies the bootloader's signature, the bootloader verifies the OS kernel, and the OS verifies application binaries. Each layer checks the next. The right-hand column lists three industrial applications where this matters: smart meters that reject unsigned firmware, medical pumps that won't actuate on unsigned code, and automotive ECUs that resist performance tuning and tampering. Break any link, and everything above it is suspect.

## Slide 7
03 · NETWORK SECURITY
CONCEPT · LECTURE 3 / 9
Confidentiality · Integrity · Authenticity
Network security in IoT ensures that data moving between devices, gateways, and the cloud cannot be read, altered, or spoofed by an attacker in the middle. The challenge is doing this on constrained devices with kilobytes of RAM and milliwatts of battery.
Confidentiality — encrypt traffic so passive observers cannot read payloads.
Integrity — MAC or AEAD so a single bit flip is detected and rejected.
Authenticity — mutual certificate-based auth, not just server-side TLS.
PROTOCOL
LAYER
TYPICAL USE
TLS 1.3
TCP / App
Cloud HTTPS, MQTT-over-TLS
DTLS 1.2
UDP / App
Constrained BLE mesh, CoAP
IPsec
IP
Site-to-site gateway tunnels
IEEE 802.1AR
Link
Device identity cert (devID)
6LoWPAN-IPHC
6LoWPAN
Header compression for IPv6 over BLE/802.15.4
⚡
LIVE EXAMPLE — The Jeep Cherokee hack (2015): researchers penetrated the cellular-to-CAN bus gateway via an unauthenticated D-Bus service over Sprint's network, remotely braking the vehicle on a highway.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
07 / 21
Notes: Network security in IoT is fundamentally about the CIA triad — confidentiality, integrity, and authenticity — applied to data in motion, often under severe resource constraints. Constrained devices cannot always afford full TLS; DTLS gives you datagram-friendly TLS, and protocols like OSCORE or CoAP-over-DTLS compress the overhead. The table on the right summarizes the core protocols you need to know: TLS 1.3 for TCP traffic, DTLS for UDP, IPsec for site-to-site tunnels, IEEE 802.1AR for device identity at the link layer, and 6LoWPAN header compression for IPv6 over low-power radios. The Jeep Cherokee hack of 2015 is the canonical network-security failure: an unauthenticated D-Bus service running inside the infotainment unit was reachable over Sprint's cellular network, and from there the attackers bridged to the internal CAN bus — remotely engaging the brakes on a moving vehicle. The lesson: every network-facing service must authenticate, even internal ones.

## Slide 8
03 · NETWORK SECURITY
Network Defense Stack — Device to Cloud
Each hop adds a control; defense in depth across the path.
STAGE 01
#
DEVICE
Constrained node
· IEEE 802.1AR devID
· DTLS to gateway
STAGE 02
◌
GATEWAY
Edge aggregator
· Mutual TLS
· Firewall rules
STAGE 03
⛨
IDS / IPS
Intrusion detect
· Snort / Suricata
· Anomaly ML
STAGE 04
⚿
FIREWALL
L4–L7 filter
· Stateful rules
· DDoS scrub
STAGE 05
☁
CLOUD
Service backend
· mTLS + OAuth
· Audit logging
▦
APPLICATIONS — THREE LIVE DEPLOYMENTS
Smart Grid — AMI meters use 802.1AR identity, DTLS to collector, IDS at substation.
Connected Vehicle — TLS to OEM cloud, IPS in gateway, anomaly ML on CAN bus.
Industrial IoT — IPsec tunnel to SCADA, DMZ IDS, segmented OT/IT networks.
IOT-SEC · 2026
NETWORK SECURITY · DEFENSE STACK
08 / 21
Notes: Network defense in IoT is best visualized as a pipeline. Data flows from the device — the most constrained, least trusted node — through a gateway that aggregates traffic and provides mutual TLS, through an intrusion-detection layer that flags anomalies, past a stateful firewall that filters by protocol and rate, and finally to a cloud backend that requires mTLS and OAuth. The key principle is defense in depth: no single control is sufficient, and each hop adds a layer. The bottom strip shows three real deployments: smart-grid AMI uses 802.1AR identity and DTLS; connected vehicles run TLS to the OEM cloud and IPS in the head unit; industrial IoT uses IPsec tunnels and a DMZ to isolate OT from IT. The same five-stage pattern recurs across domains — only the protocols change.

## Slide 9
04 · GENERIC APPLICATION SECURITY
OWASP IoT Top Vulnerabilities & Controls
Application-level security is independent of the device underneath. These six controls defend the application logic itself — and map directly onto the OWASP IoT Top 10.
01
⚿
Authentication
Mutual certificate-based auth; no hardcoded passwords; MFA for admin portals.
02
⛨
Authorization
Per-device RBAC; least-privilege scopes; refresh-token rotation.
03
✓
Input Validation
Schema-validated payloads; canonical parsing; reject unbounded JSON.
04
⚿
Cryptography
AES-256-GCM at rest; TLS 1.3 in transit; HKDF for key derivation.
05
◆
Secure Update
Signed firmware images; rollback protection; staged A/B partitions.
06
✦
Logging & Audit
Tamper-evident logs; SIEM ingestion; alert on anomaly.
◖
LIVE EXAMPLE — The 2021 Verkada breach: attackers used a hardcoded super-admin credential in the cloud app to access 150K+ live security cameras across hospitals, jails, and Tesla factories.
IOT-SEC · 2026
APPLICATION SECURITY · CONCEPT
09 / 21
Notes: Generic application security is the layer of defenses that sit inside your application logic — independent of the device, network, or OS underneath. These six controls are the minimum bar: authentication must be mutual and certificate-based, never hardcoded passwords; authorization uses per-device RBAC with least privilege; input validation rejects malformed JSON and bounds untrusted sizes; cryptography uses AES-256-GCM at rest and TLS 1.3 in transit, with HKDF for any key derivation; secure update means signed firmware with rollback protection, ideally A/B partitions; and logging must be tamper-evident, fed to a SIEM, and trigger alerts on anomalies. The 2021 Verkada breach shows what happens when authentication fails: a single hardcoded super-admin credential gave attackers access to 150,000 live cameras in hospitals, jails, and Tesla factories. Six controls — every one must hold.

## Slide 10
04 · NETWORK SECURITY → APPLICATION
Application Security — Layered Controls
A defense-in-depth stack — each layer is independently testable.
LAYER 5
IDENTITY & ACCESS
OAuth 2.0 · OIDC · X.509 mTLS · SCIM
LAYER 4
CRYPTOGRAPHY
AES-256-GCM · TLS 1.3 · ECDSA P-256 · HKDF-SHA256
LAYER 3
INPUT & API
JSON Schema · OpenAPI · regex allowlist · rate-limit
LAYER 2
UPDATE & OTA
Signed manifests · TUF · Uptane · A/B partitions
LAYER 1
LOGGING & AUDIT
Append-only log · SIEM · immutable WORM storage
LIVE EXAMPLE
Stuxnet (2010) exploited weak update verification on Siemens S7-300 PLCs. The worm presented a forged WinCC driver signature, bypassing Layer 2 controls and ultimately damaging ~1,000 centrifuges at the Natanz facility.
App — Industrial Control
IOT-SEC · 2026
APPLICATION SECURITY · LAYERED STACK
10 / 21
Notes: The application security stack is built like a pyramid. At the base is logging and audit — your ability to see what happened after the fact. Above that, secure update — because the OTA channel is the single most common way attackers get code execution onto devices. Above that, input and API validation — the front door attackers probe. Above that, cryptography — encrypting data at rest and in transit. At the top, identity and access — the gatekeeper. Stuxnet is the canonical example: the worm forged driver signatures on Siemens WinCC software, effectively bypassing the update layer (Layer 2) on S7-300 PLCs. Once inside, it modified the centrifuge control logic and destroyed about 1,000 centrifuges at the Natanz enrichment facility. Any one layer can be bypassed — which is exactly why defense in depth matters.

## Slide 11
05 · APPLICATION PROCESS SECURITY & SAFETY
Security Meets Functional Safety
Process security is the discipline of preventing application-layer failures from causing physical harm. It is where cybersecurity meets functional safety — combining IEC 61508 (industrial) and ISO 26262 (automotive) with security controls to ensure that a hacked device fails safe, not dangerous.
✦
SIL — Safety Integrity Level (1–4) sets the maximum tolerated probability of dangerous failure per hour.
⚡
SIF — Safety Instrumented Function is the specific function (e.g. emergency stop) that must execute on demand.
⚠
Hazard Analysis — HAZOP / FMEA identify failure modes; security threats are then layered on top.
⛨
SIL CLASSIFICATION
SIL 4
Catastrophic · Nuclear, aviation
PFD < 10⁻⁴
SIL 3
Severe · Railway signalling, refinery
PFD < 10⁻³
SIL 2
Serious · Industrial boiler, escalator
PFD < 10⁻²
SIL 1
Minor · HVAC, lighting
PFD < 10⁻¹
⚠
LIVE EXAMPLE — Therac-25 (1986): a software race condition in a radiation-therapy machine delivered lethal overdoses to 6 patients. No hardware interlock existed because developers trusted software alone — a SIL-4 system built without defense in depth.
IOT-SEC · 2026
PROCESS SAFETY · CONCEPT
11 / 21
Notes: Process security is the intersection of cybersecurity and functional safety. A device can be perfectly secure against remote attackers and still kill someone if its safety logic fails. The SIL framework — Safety Integrity Level, defined in IEC 61508 — quantifies how reliable a safety function must be, expressed as Probability of Failure on Demand (PFD). SIL 1 tolerates a 1-in-10 chance per demand; SIL 4 tolerates 1-in-10,000. The right column shows real applications: nuclear and aviation need SIL 4; railway signalling and refineries need SIL 3; industrial boilers and escalators are SIL 2; HVAC and lighting are typically SIL 1. The Therac-25 case from 1986 is the textbook disaster: developers removed hardware interlocks, trusting software alone. A race condition caused the electron beam to deliver 100× the intended dose — killing six patients. Software-only safety is never enough. Always add a hardware interlock.

## Slide 12
05 · PROCESS SAFETY
IEC 61508 Safety Lifecycle
From hazard discovery to decommissioning — security and safety are joined throughout.
STAGE 1
⚠
HAZARD ID
HAZOP / FMEA workshop
STAGE 2
#
RISK ASSESS
Risk matrix, ALARP
STAGE 3
▣
SIL ALLOC
Assign SIL 1–4 to each SIF
STAGE 4
#
DESIGN
Sensors, logic solver, final element
STAGE 5
✓
VALIDATE
FAT, SAT, proof testing
STAGE 6
▶
OPERATE
Maintain, audit, decommission
CONTINUOUS IMPROVEMENT
RE-EVALUATE ON INCIDENT / FIRMWARE UPDATE
▦
APPLICATIONS
Oil & Gas — Emergency Shutdown (ESD) systems at SIL 3.
Automotive — ISO 26262 ASIL derived from IEC 61508.
Medical — IEC 62304 lifecycle for medical device software.
IEC 61508 / ISO 26262
IOT-SEC · 2026
PROCESS SAFETY · LIFECYCLE
12 / 21
Notes: The IEC 61508 safety lifecycle is the gold standard for any safety-critical IoT system. It begins with hazard identification — a HAZOP or FMEA workshop where engineers systematically walk through every operating mode and ask what could go wrong. Step two is risk assessment: scoring each hazard on a risk matrix and asking whether the residual risk is ALARP — As Low As Reasonably Practicable. Step three allocates SIL levels to each Safety Instrumented Function. Step four is design: choosing sensors, the logic solver, and the final actuator. Step five is validation — Factory Acceptance Test, Site Acceptance Test, and periodic proof testing. Step six is operation: ongoing maintenance, audit, and eventual decommissioning. The dashed feedback loop is essential: every incident, every firmware update, every new threat should trigger re-evaluation. Without that loop, the safety case drifts out of sync with reality.

## Slide 13
06 · RELIABLE & SECURE BY DESIGN
Shift Security Left — Build It In, Don't Bolt It On
Secure-by-design treats security and reliability as architectural first principles, not as patches applied after shipping. The cost of fixing a vulnerability grows ~30× from design to deployment.
01
⛨
Threat Model
STRIDE / DREAD before code
02
⚿
Least Privilege
Minimal permissions, minimal surface
03
✦
Defense in Depth
Multiple independent controls
04
⚿
Secure Defaults
Deny by default, opt-in features
05
✓
Verify, Don't Trust
Validate at every boundary
06
▣
Bill of Materials
SBOM for every dependency
07
✦
Auditability
Tamper-evident logs, traceable builds
COST TO FIX A DEFECT
DESIGN
$1
TESTING
$30
PRODUCTION
$1,000+
IOT-SEC · 2026
SECURE BY DESIGN · CONCEPT
13 / 21
Notes: Secure-by-design is the philosophy that security and reliability must be architectural properties — baked in from day one, not bolted on after a breach. The seven principles on this slide are the operating contract. Threat-model before you write code, using STRIDE or DREAD. Apply least privilege — every component, device, and user gets the minimum access needed. Layer your defenses so that no single failure is catastrophic. Ship secure defaults — deny-by-default, opt-in for any risky feature. Verify, don't trust — validate at every boundary, even internal ones. Maintain a Software Bill of Materials so you know what's in your firmware when a Log4Shell-style vulnerability drops. And make everything auditable: tamper-evident logs, reproducible builds, signed artifacts. The three chips at the bottom tell the economic story: a defect costs a dollar at design time, thirty at test, and over a thousand in production. Shift left.

## Slide 14
06 · SECURE BY DESIGN
Secure-by-Design Development Lifecycle
A 7-stage DevSecOps loop — security activities at every stage.
STAGE 1
⛨
THREAT MODEL
· STRIDE / DREAD
· Attack trees
STAGE 2
▤
REQUIREMENTS
· Security NFRs
· Compliance (GDPR)
STAGE 3
#
ARCHITECTURE
· Layered design
· Trust boundaries
STAGE 4
#
IMPLEMENT
· Secure coding
· Code review, SAST
STAGE 5
#
TEST
· DAST, fuzz
· Pen test
STAGE 6
➤
DEPLOY
· Signed images
· IaC scan
STAGE 7
♥
OPERATE
· Runtime IDS
· Patch, audit
CONTINUOUS FEEDBACK
▦
APPLICATIONS — REAL-WORLD DEPLOYMENTS
Smart Home — Google Nest applies threat modeling per device class, automated SAST in CI, signed OTA, runtime IDS reporting to fleet telemetry.
Automotive — Tesla ships signed firmware every 2 weeks, A/B partitions for rollback, bug-bounty program feeding threat models.
Medical — Medtronic insulin pumps use IEC 62304 lifecycle, pre-market security review by FDA, post-market patching under coordinated disclosure.
IOT-SEC · 2026
SECURE BY DESIGN · LIFECYCLE
14 / 21
Notes: The secure-by-design lifecycle turns the seven principles into operational practice. We move left-to-right through seven stages, each with its own security activity. We start with threat modeling — using STRIDE to enumerate spoofing, tampering, repudiation, information disclosure, denial of service, and elevation of privilege. We capture security requirements as NFRs and verify them against compliance regimes like GDPR. We design the architecture with explicit trust boundaries — every boundary is a place where we validate. We implement with secure coding standards, mandatory code review, and static analysis (SAST). We test with dynamic analysis (DAST), fuzzing, and external pen tests. We deploy only signed images, scanned Infrastructure-as-Code. And we operate with runtime IDS, patching, and audit. The feedback loop is critical: every runtime incident feeds the next threat model. The bottom strip shows three real deployments — Google Nest, Tesla, and Medtronic — each implementing this lifecycle.

## Slide 15
07 · RUN-TIME MONITORING
CONCEPT · LECTURE 7 / 9
Detect, Respond, Recover — In Real Time
Run-time monitoring is the practice of continuously observing live system behavior to detect attacks, anomalies, and policy violations as they happen — then responding before damage spreads. Static security catches known bad patterns; runtime security catches what static analysis cannot.
IDS — Intrusion Detection Systems inspect traffic and process behavior against rules + ML models.
Anomaly Detection — baseline normal telemetry, flag deviations beyond 3σ or model-scored thresholds.
Automated Response — isolate device, revoke credentials, push signed patch — without human latency.
MONITORING TECHNIQUES
HIDS
Host-based — file integrity, process tree, syscall audit
NIDS
Network-based — packet inspection, flow analysis
ML-IDS
Unsupervised ML on telemetry streams (autoencoders, isolation forest)
EBPF
Linux kernel probes — syscall-level tracing with zero overhead
⚡
LIVE EXAMPLE —Target 2013 breach: HVAC vendor credentials, stolen via a phishing email, were used to infiltrate Target's network. The installed FireEye IDS detected the malware and alerted — but the security team ignored the alerts because they were tuned to false positives. 40M credit cards were stolen.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
15 / 21
Notes: Run-time monitoring is the eyes and ears of a security program. Static analysis catches known-bad signatures before code ships; runtime monitoring catches everything else — zero-days, insider threats, the unknown unknowns. The two main flavors are HIDS, host-based, watching files, processes, and syscalls, and NIDS, network-based, watching packets and flows. Modern systems layer ML-based anomaly detection on top, learning the normal baseline of telemetry and flagging deviations beyond three sigma or what an autoencoder can reconstruct. eBPF traces syscalls at kernel level with near-zero overhead. But detection alone is worthless without response — the 2013 Target breach is the painful lesson: their FireEye IDS detected the malware and alerted correctly, but the security team, drowning in false positives, ignored the alerts. Forty million credit cards were stolen because alerts were ignored, not because detection failed. Alerts must be actionable, tuned, and owned.

## Slide 16
07 · RUN-TIME MONITORING
Run-Time Monitoring Architecture
Sense → Collect → Analyze → Decide → Act — closed-loop response.
BLOCK DIAGRAM
01
#
SENSE
● Syscall audit
● Flow capture
● File integrity
02
↑
COLLECT
● Edge agent
● Pub-Sub bus
● Time-series DB
03
▦
ANALYZE
● Rule engine
● ML scoring
● Threat intel feed
04
▤
DECIDE
● Risk scoring
● Alert routing
● Playbook match
05
⚡
ACT
● Isolate device
● Revoke cert
● Push patch
●POST-INCIDENT LEARNING — UPDATE MODELS, REFINE RULES
APPLICATIONS — LIVE DEPLOYMENTS
❄
Smart Grid
PMU sensors stream to regional collector; ML detects FDI (False Data Injection) attacks on state estimation.
Connected Fleet
Each vehicle uploads CAN-bus anomalies to the OEM SOC; SELinux audit logs trip HIDS rules.
Hospital IoT
Medical-device IDS (e.g. Cynerio) fingerprints infusion pumps and flags protocol deviations in real time.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
16 / 21
Notes: Runtime monitoring is a closed loop. Stage one is sensing — syscall audit logs on hosts, packet captures on the network, file-integrity monitors on critical binaries. Stage two is collection — an edge agent ships data to a pub-sub bus, landing it in a time-series database. Stage three is analysis: a rule engine matches known-bad patterns, an ML model scores deviations, a threat-intel feed correlates with IOCs observed elsewhere. Stage four is decision — risk-scoring the alert, routing it to the right team, matching against a playbook. Stage five is action: isolate the device, revoke its certificate, push a signed patch. The dashed feedback loop is critical: after every incident, the analysis models are retrained and the rules refined. The bottom strip shows three live deployments — smart-grid PMU sensing detects False Data Injection attacks; connected vehicles stream CAN-bus anomalies; hospital IoT fingerprints infusion pumps and flags protocol deviations.

## Slide 17
08 · THE ARMET APPROACH
CONCEPT · LECTURE 8 / 9
Hardening Methodology for Microcontrollers
ARMET — a hardening Approach for Reliable and secure Microcontrollers in IoT by applicaTion — is a structured, application-aware methodology for reducing the attack surface of resource-constrained IoT devices. Rather than applying generic hardening checklists, ARMET selects controls based on the application's threat model and the device's hardware capabilities.
Application-Aware — threat model per device class drives control selection.
Capability-Driven — chooses hardening based on what the silicon actually supports (TEE, crypto engine, MPU).
Verifiable — each hardening step produces an artifact testable in CI/CD, not a doc-only deliverable.
Example target — ESP32-class microcontroller with on-chip crypto, secure boot, and flash encryption.
COMPONENT 1
Threat Modeling — STRIDE per application context
COMPONENT 2
Hardening Catalog — 7 control categories mapped to capabilities
COMPONENT 3
Verification — Test harness in CI/CD proving each control
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
17 / 21
Notes: ARMET — the name encodes its purpose: a hardening Approach for Reliable and secure Microcontrollers in IoT by applicaTion. It is a methodology, not a product. The core insight: generic hardening checklists like CIS Benchmarks were written for servers with megabytes of RAM and dedicated security teams — they do not map onto a 32-bit microcontroller with 512K of flash and no full OS. ARMET fixes this with three components. First, threat modeling per application context — a smart lock has a different threat model from a soil sensor, even on identical hardware. Second, a hardening catalog of seven control categories — secure boot, crypto, key storage, network, memory protection, update, logging — each mapped to silicon capabilities. Third, verification — every control produces a CI/CD-testable artifact, so hardening is enforced by build pipeline, not by documentation. The image shows a typical ARMET target: an ESP32-class MCU with on-chip crypto, secure boot, and flash encryption.

## Slide 18
08 · THE ARMET APPROACH
ARMET — 7-Step Hardening Methodology
A linear pipeline feeding a continuous-improvement feedback loop.
BLOCK DIAGRAM
01
▣
ASSET INVENTORY
Enumerate device, OS, libs, data
02
⛨
THREAT MODEL
STRIDE per application context
03
▦
CAPABILITY MAP
TEE, crypto, MPU, secure boot
04
✓
CONTROL SELECT
Choose hardening per asset+threat
05
⚒
IMPLEMENT
Apply configs, code, key provisioning
06
✓
VERIFY
CI tests prove each control holds
07
♥
OPERATE
Monitor, re-harden on incident
RE-EVALUATE THREAT MODEL · BACK TO STAGE 2
CONTROL CATEGORIES
Secure Boot
Crypto & Keys
Network Hardening
Memory Protection
Secure Update
Logging & Audit
Physical Tamper
⚡
APPLICATION —Smart-Lock vendor deploys ARMET: threat model identifies relay attacks; capability map shows ESP32 has AES + secure boot; controls select authenticated BLE + signed firmware; CI verifies signatures on every build; runtime monitors door-actuator anomalies.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
18 / 21
Notes: The ARMET methodology runs as a seven-step pipeline. Step one: inventory — what device, OS, libraries, data flows. Step two: threat model using STRIDE, scoped to the application context — a smart lock cares about relay attacks, a soil sensor about data tampering. Step three: map hardware capabilities — TEE, crypto accelerator, MPU, secure boot. Step four: select controls from the seven-category catalog on the right. Step five: implement — configs, code, key provisioning. Step six: verify in CI — every control produces a testable artifact; if secure boot is supposed to be on, the pipeline must fail when it is off. Step seven: operate — runtime monitoring, and crucially, re-evaluate the threat model after every incident. The bottom example shows a smart-lock vendor deploying ARMET end-to-end: relay attacks in the threat model, ESP32 capabilities drive control selection, CI verifies signatures on every build, runtime monitors door-actuator anomalies. ARMET turns hardening from a checklist into an engineering pipeline.

## Slide 19
09 · PRIVACY & DEPENDABILITY
CONCEPT · LECTURE 9 / 9
Beyond Security — Privacy, Reliability, Availability, Safety
Dependability is the umbrella property that encompasses reliability, availability, safety, and security. Privacy is the additional promise that personal data is collected, processed, and retained only with user consent and only for stated purposes — a regulated expectation under GDPR, CCPA, and similar frameworks.
Dependability attributes — Reliability (MTBF), Availability (uptime), Safety (no harm), Security (no breach), Maintainability.
Privacy principles — Data minimization, purpose limitation, consent, right to erasure, end-to-end encryption.
Fault → Error → Failure — A fault (bug/attack) becomes an error (wrong state) becomes a failure (service unavailable).
Privacy is a hardening outcome — the padlock is only as strong as the weakest control.
KEY REGULATIONS
⚖
GDPR (EU)
€20M or 4% of global revenue, max fine
CCPA / CPRA (CA)
$7,500 per intentional violation
IoT Act (US)
NIST baseline for federal IoT — IoT Cybersecurity Improvement Act
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
19 / 21
Notes: The final topic widens the lens beyond security to two interlocking properties: dependability and privacy. Dependability is the umbrella term that encompasses reliability — Mean Time Between Failures; availability — uptime; safety — the absence of physical harm; security — the absence of unauthorized access; and maintainability — the ease of repair. A device can be perfectly secure and yet unreliable; highly available and yet unsafe. Privacy is the additional promise that personal data is collected minimally, used only for stated purposes, encrypted end-to-end, and erasable on request. GDPR has made privacy a regulated expectation, with fines up to twenty million euros or four percent of global revenue — whichever is higher. The image of the hardened padlock captures the philosophy: privacy is a hardening outcome, and the chain is only as strong as the weakest link. The classic mental model is the fault-error-failure chain — dependability engineering breaks that chain before the failure.

## Slide 20
09 · PRIVACY & DEPENDABILITY
Dependability & Security — Unified Threat Tree
How faults cascade to failures — and where controls intervene.
BLOCK DIAGRAM
✦
FAULT
Bug, attack, hardware defect
Fault prevention
coding standards, secure boot
⊗
ERROR
Wrong internal state
Error detection
MPU, runtime IDS
⚠
FAILURE
Service deviates from spec
Fail-safe design
interlocks, redundancy
⚠
HAZARD
Potential for harm
DEPENDABILITY ATTRIBUTES — FIVE PILLARS
◉
⛨
RELIABILITY
MTBF, MTTR
☁
AVAILABILITY
99.999% uptime
✚
SAFETY
No physical harm
⚿
SECURITY
CIA triad held
⚒
MAINTAINABILITY
Easy to patch
Application — Medical device must satisfy all 5; consumer wearable trades off SIL.
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
20 / 21
Notes: The dependability tree shows how attacks become harm — and where controls intervene. The cascade starts with a fault, which can be a software bug, an attack, or a hardware defect. The fault produces an error — an incorrect internal state — which propagates to a failure, where the service deviates from its specification, which can become a hazard, exposing a user to physical harm. Each arrow is where a control breaks the chain. Fault prevention — secure coding standards, secure boot, signed updates — stops faults from entering the system. Error detection — MPU isolation, runtime IDS, canaries — catches errors before they become failures. Fail-safe design — hardware interlocks, redundant sensors, graceful degradation — ensures the device fails safe. Below the cascade, the five dependability attributes form the engineering checklist. A medical device must satisfy all five; a consumer wearable can trade off safety integrity against cost — but the trade-off must be explicit, documented, and reviewed.

## Slide 21
SUMMARY · TAKEAWAYS
Nine Concepts, One Secure Stack
IoT security is a layered, lifecycle discipline. Each concept reinforces the next — from the silicon root of trust to the privacy promises you make to your users.
01 — 03
Foundation (Topics 1-3)
● Layered architecture — perception, network, application
● Hardware root of trust anchors every higher layer
● Mutual auth, TLS 1.3, IDS in every network hop
04 — 06
Application (Topics 4-6)
● Six controls — authN, authZ, crypto, validation, OTA, logging
● Process safety — SIL/SIF and the IEC 61508 lifecycle
● Secure-by-design — shift left, threat-model first
07 — 09
Operation (Topics 7-9)
● Runtime monitoring — sense, analyze, decide, act, learn
● ARMET — application-aware 7-step hardening pipeline
● Privacy + dependability — the user-facing promises
Build it in. Verify it holds. Watch it run. Patch it before the attacker does.
IOT-SEC · COURSE NOTES · 09 TOPICS · 21 SLIDES
RELIABLE & SECURE IOT APPLICATIONS · IOT-SEC 2026
21 / 21
Notes: To wrap up: IoT security is not a single technology but a layered, lifecycle discipline. The nine concepts we covered form three clusters. The foundation — introduction, systems security, network security — establishes the layered architecture, the hardware root of trust, and the network defenses that everything else depends on. The application cluster — generic application security, process safety, secure-by-design — covers the six application-layer controls, the IEC 61508 safety lifecycle, and the shift-left philosophy. The operation cluster — runtime monitoring, ARMET, and privacy/dependability — covers how you watch the running system, how you systematically harden microcontrollers, and the dependability and privacy promises you keep with your users. The closing line says it all: build it in, verify it holds, watch it run, patch it before the attacker does. Four verbs, one practice. Thank you.